ARP-DHCP
From Liebeherr / El-Zarki Lecture Notes

---
ARP (Address Resolution Protocol)

---
ARP and RARP

---
Address Translation with ARP

---
Address Translation with ARP

---
ARP Packet Format

---
Example
ARP Request from Argon:
Source hardware address:
Source protocol address:
Target hardware address:
Target protocol address:
ARP Reply from Router137:
Source hardware address:
Source protocol address:
Target hardware address:
Target protocol address:
00:a0:24:71:e4:44
128.143.137.144
ff:ff:ff:ff:ff:ff
128.143.137.1
Target hardware address is unknown thus the broadcast
00:e0:f9:23:a8:20
128.143.137.1
00:a0:24:71:e4:44
128.143.137.144

---
ARP Cache

---
Things to know about ARP

---
ARP Vulnerabilities

---
DHCP
(Dynamic Host Configuration Protocol)

---
Dynamic Assignment of IP addresses
Dynamic assignment of IP addresses is desirable for several reasons:
- IP addresses are assigned on-demand
- Avoid manual IP configuration
- Support mobility (laptops, phones, IoTs devices, ...)
Three Protocols:
- RARP (until 1985, no longer used)
- BOOTP (1985-1993)
- DHCP (since 1993)
Only DHCP is widely used today.

---
Solutions for dynamic assignment of IP addresses
Reverse Address Resolution Protocol (RARP)
- RARP is no longer used
- Works similar to ARP
- Broadcast a request for the IP address associated with a given MAC address
- RARP server responds with an IP address
- Only assigns IP address (not the default router and subnetmask)

---
BOOTP
BOOTstrap Protocol (BOOTP)
- Host can configure its IP parameters at boot time.
- Not only assigns IP address, but also default router, network mask, etc.
- Client sends UDP message (src addr 0.0.0.0) to server listening on port 67.
- Server responds with IP address to be given to the client that is listening on port 68.
- Use limited broadcast address (255.255.255.255):
- These addresses are never forwarded

---
DHCP
Dynamic Host Configuration Protocol (DHCP)
- Designed in 1993
- An extension of BOOTP (Many similarities to BOOTP)
- Same port numbers as BOOTP
- Extensions:
- Supports temporary allocation (“leases”) of IP addresses
- DHCP client can acquire all IP configuration parameters
- DHCP is the preferred mechanism for dynamic assignment of IP addresses
- DHCP can interoperate with BOOTP clients.

---
DHCP Messages
Capturing DHCP exchanged messages using wireshark at the Asus user

---
DHCP exchanged messages

---
DHCP Discover

---
DHCP Discover (Details)

---
DHCP Offer

---
DHCP Offer (Details)

---
DHCP Request

---
DHCP Request (Details)

---
DHCP Acknowledge

---
DHCP Acknowledge (Details)

---
DHCP/BOOTP Message format
(There are >100 different options)

---
DHCP/BOOTP
OpCode: 1 (Request), 2(Reply)
 Note: DHCP message type is sent in an option
Hardware Type: 1 (for Ethernet)
Hardware address length: 6 (for Ethernet)
Hop count: set to 0 by client
Transaction ID: Integer (used to match reply to response)
Seconds: number of seconds since the client started to boot
Client IP address, Your IP address, server IP address, Gateway IP address, client hardware address, server host name, boot file name:
client fills in the information that it has, leaves rest blank

---
DHCP Message type
Value	Message Type
1	DHCPDISCOVER
2	DHCPOFFER
3	DHCPREQUEST
4	DHCPDECLINE
5	DHCPACK
6	DHCPNAK
7	DHCPRELEASE
8	DHCPINFORM
Message type is sent as an option

---
Other DHCP Options
Other DHCP information that is sent as an option:
Subnet Mask, Name Server, Hostname, Domain Name, Forward On/Off, Default IP TTL, Broadcast Address, Static Route, Ethernet Encapsulation, X Window Manager, X Window Font, DHCP Msg Type, DHCP Renewal Time, DHCP Rebinding, Time SMTP-Server, SMTP-Server, Client FQDN, Printer Name, …