## Slide 1: Application layer
Networks and Protocols

## Slide 2: Principles of network applications
Chapter 02: Application layer

## Slide 3
Implementation of each protocol layer is located in either the
  user-space,
  kernel-space, or
  the device (hardware)
Application layer allows people to use the Internet,
Other 4 layers are just made so people can use application programs.
Physical
Device
Application
Transport
Network
Data Link
Kernel
User
user
Programs
How to implement a network application?

## Slide 4
Design the architecture
  which process does what?
Design the communication protocol
  what sequences of messages can be exchanged?
Choose the transport-layer technology
  what will the application expect from the transport layer?
Design an application

## Slide 5
Client-server paradigm
  server:
    always-on host
    permanent IP address
    often in data centers, for scaling
  clients:
    contact, communicate with server
    may be intermittently connected
    may have dynamic IP addresses
    do not communicate directly with each other
    examples: HTTP, IMAP, FTP
Design the architecture
Server
Client
a process that generates service requests
May be via Internet or not
a process that is always running reachable at a fixed, known process name answers service requests
Notes: By the way, people often use the term “server” to refer not only to the server process, but to an entire computer that is running server processes in its application layer.
When an application uses the client/server architecture, we usually end up with a picture including many clients

## Slide 6
Peer-Peer architecture
  a process that may both generate and answer requests
  no always-on server
  arbitrary end systems directly communicate
  peers request service from other peers, provide service in return to other peers
    self scalability – new peers bring new service capacity, as well as new service demands
  peers are intermittently connected and change IP addresses
    complex management
  example: P2P file sharing
Design the architecture
Peer
Peer
May be via Internet or not

## Slide 7
We need a “door” so that a network application can send/receive messages to/from the network
The door should appear between the user space and kernel space so that details of the kernel space can be hidden
Socket is the door!
Design the communication protocol
Device
Application
Transport
Kernel
User
Client/Server
Program
What is the interface?

## Slide 8
A socket is a host-local, application-created, OS-controlled interface (a “door”) into which application process can both send and receive messages to/from another application process
  Similar to a file descriptor, which interfaces between an application and a file
One socket is tied to one application process (or thread)
  An application can create many processes (and hence sockets)
Socket
Device
Kernel
Client/Server
Program
Socket
Socket
Socket
TCP Control
UDP Control

## Slide 9
To receive messages, process must have identifier
Idea: use the unique 32-bit IP address of host device
  But, does IP address of host on which process runs suffice for identifying the process?
  no, many processes can be running on same host
Idea: Use another identifier with the IP address
  (IP address, port number)= Socket
  Analogous to mailing a letter to a professor in a department:
    IP address is the address of the department
    Port number is the mail box of the professor
  Example of port numbers:
    HTTP server: 80
    mail server: 25
Addressing processes
Device
Kernel
Client/Server
Program
Socket
Socket
Socket
TCP Control
UDP Control

## Slide 10
Addressing processes
Host Computer
IP Address
MAC Layer
LLC Layer
Network Layer (IP Layer)
Transport Layer (TCP Layer)
Process D
Process C
Process B
Process A
ports
1045
9133
6055
12133
Physical Layer
Datalink Layer
Host Computer

## Slide 11
Reliable data delivery
  Deliver message to the destination process or signal failure
  detect and recover from packet loss or corruption
  loss-sensitive applications (e.g., web, file transfer, email, …)
Guaranteed performance
  Minimum throughput
    throughput-sensitive applications (e.g., video-conferencing)
  Maximum end-to-end packet delay
    delay-sensitive applications,(e.g., emergency services, voice, gaming, …),
Guaranteed security
  Confidentiality: message is revealed only to the destination
  Authenticity: message indeed came from claimed source
  Data integrity: message is not changed along the way
Choose the transport-layer technology

## Slide 12
TCP: Transmission Control Protocol
  reliable,
  in-order data delivery,
  flow control,
  congestion control.
  TCP is “connection-oriented” or “stateful” = maintains state on all the local/remote process pairs that use TCP (uses memory).
UDP: User Datagram Protocol
  detection of packet corruption.
  UDP is “connection-less” or “stateless” = does not maintain state on remote processes (memory less).
No protocol offering guaranteed performance
Internet transport-layer protocols

## Slide 13
application
file transfer/download
e-mail
Web documents
real-time audio/video
streaming audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5Kbps-1Mbps
video:10Kbps-5Mbps
same as above
Kbps+
elastic
time sensitive?
no
no
no
yes, 10’s msec
yes, few secs
yes, 10’s msec
yes and no
Transport service requirements: common apps

## Slide 14
application
file transfer/download
e-mail
Web documents
Internet telephony
streaming audio/video
interactive games
application
layer protocol
FTP [RFC 959]
SMTP [RFC 5321]
HTTP 1.1 [RFC 7320]
SIP [RFC 3261], RTP [RFC 3550], or proprietary HTTP [RFC 7320], DASH
WOW, FPS (proprietary)
transport protocol
TCP
TCP
TCP
TCP or UDP
TCP
UDP or TCP
Internet applications, and transport protocols

## Slide 15: DNS - Domain Name System
Chapter 02: Application layer

## Slide 16
If you need to reach Google, you need their IP
  Does anyone know Google’s IP?
Problem:
  People can’t remember IP addresses (e.g. 129.10.117.100)
  Need human readable names (e.g. www.google.com, www.ensia.edu.dz ) that map to IPs.
Solution:
  Use Domain Name System (DNS)
    DNS provides a mapping between symbolic names and IP addresses (and further services).
    DNS also provides inverse look up that maps an IP address to symbolic names.
DNS: Introduction

## Slide 17
Before DNS, all mappings were in hosts.txt
  /etc/hosts on Linux
  C:\Windows\System32\drivers\etc\hosts on Windows
Machines periodically FTP new copies of hosts.txt
Centralized, manual system
  single point of failure
  traffic volume
    Number of DNS queries/day is very important
  Maintenance
  No scalable
Thus, In 1983, the first stable operational DNS was born
DNS: History

## Slide 18
Domain Name System
Distributed database
  i.e. the individual segments are subject to local control
The structure of the used name space of the database shows the administrative organization of the Internet
Data of each local area are available by means of a simple Client/Server architecture
Robustness and speed of the system are being achieved by replication and caching of the naming data
Hierarchical namespace
  As opposed to original, flat namespace
  e.g. .com  google.com  mail.google.com
Structure of the Database

## Slide 19
Name Server: Server which manages information about a part of the database
Resolver: Client which requests naming information from the server
DNS: Main components

## Slide 20
Hierarchical namespace
“Top Level Domains” are at the top Domains are subtrees
  e.g., .edu, umich.edu, eecs.umich.edu
Name is leaf-to-root path
  cse.eecs.umich.edu
Depth of tree is arbitrary (limit 128)
Name collisions trivially avoided
  Each domain is responsible
root
us
com
gov
mil
org
net
eg
dz
edu
mesrs
ensia
ESI
ISE
…

## Slide 21
Hierarchical administration
Tree is divided into zones
  Each zone has an administrator
  Responsible for the part of the hierarchy
Example
  mesrs controls names: *.mesrs.dz
  ensia controls names: *.ensia.edu.dz
root
us
com
gov
mil
org
net
eg
dz
edu
mesrs
ensia
ESI
ISE
…
ICANN/IANA
Notes: ICANN (Internet Corporation for Assigned Names and Numbers) manages root DNS domain

## Slide 22
Root servers (Top of hierarchy):
  Location hardwired into other servers
Top-level domain (TLD) servers (Next Level):
  .com, .edu, etc.
  Managed professionally
Authoritative DNS servers (Bottom Level):
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority
Server hierarchy

## Slide 23
Functions of each DNS server:
  Authority over a portion of the hierarchy
    No need to store all DNS names
  Store all the records for hosts/domains in its zone
    May be replicated for robustness
  Know the addresses of the root servers
    Resolve queries for unknown names
Root servers know about all TLDs
  The buck stops at the root servers
Server hierarchy

## Slide 24
13 logical root name “servers” worldwide each “server” replicated many times (~200 servers in US)
13 root servers, labeled AM
6 are anycasted, i.e. they are globally replicated
Contacted when names cannot be resolved
In practice, most systems cache this information
DNS Root
Notes: Actually, in Algeria there are 3 in (Algiers, Annaba and Oran)

## Slide 25
When host makes DNS query, it is sent to its local DNS server
  Local DNS server returns reply, answering:
    from its local cache of recent name-to-address translation pairs (possibly out of date!)
    forwarding request into DNS hierarchy for resolution
  Each ISP has local DNS name server; to find yours:
    Windows: >ipconfig /all
Local DNS server doesn’t strictly belong to hierarchy
local DNS server

## Slide 26
Recursive name resolution
  Puts the burden of resolution on the contacted name server (Ask server to do it for you)
  heavy load at upper levels of hierarchy?
Root
com
ns1.google.com
www.google.com
dns.cerist.dz
Where is www.google.com?
DNS name resolution

## Slide 27
Iterative name resolution
  Contact server replies with the name of the next authority in the hierarchy.
  “I don’t know this name, but this other server might”.
  This is how DNS works today.
Root
com
ns1.google.com
www.google.com
dns.cerist.dz
Where is www.google.com?
DNS name resolution

## Slide 28
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires
DNS caching

## Slide 29: DNS servers store resource records (RRs) RR is (name, value, type, TTL)
Type = NS: ( Name Server)
  name = domain
  value = hostname of authoritative name server for this domain
Type = A: ( Address)
  name = hostname
  value = IP address
DNS records
Type = MX: ( Mail eXchanger)
  name = domain in email address
  value = name of SMTP mail server associated with name
type=CNAME ( Canonical Name)
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really servereast.backup2.ibm.com
  value is canonical name

## Slide 30
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
message header:
  identification: 16 bit # for query, reply to query uses same #
  flags:
      query or reply
      recursion desired
      recursion available
      reply is authoritative
  name, type fields for a query
  RRs in response to query
  records for authoritative servers
  additional “ helpful” info that may be used
DNS protocol messages
identification
flags
questions (variable # of questions)
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)

## Slide 31
$ dig +norecurse eecs.berkeley.edu @198.41.0.4
DNS Lookup Walkthrough
Use the dig utility in your terminal, and remember to set the +norecurse flag so you can traverse the name server hierarchy yourself.
We are performing a DNS lookup for the IP address of eecs.berkeley.edu.
DNS queries always start with a request to the root name server. The IP address of the root name server is usually hard-coded into recursive resolvers.

## Slide 32
$ dig +norecurse eecs.berkeley.edu @198.41.0.4
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 26114
;; flags: qr; QUERY: 1, ANSWER: 0, AUTHORITY: 13, ADDITIONAL: 27
;; QUESTION SECTION:
;eecs.berkeley.edu. IN A
;; AUTHORITY SECTION:
edu. 172800 IN NS a.edu-servers.net.
edu. 172800 IN NS b.edu-servers.net.
edu. 172800 IN NS c.edu-servers.net.
...
;; ADDITIONAL SECTION:
a.edu-servers.net. 172800 IN A 192.5.6.30
b.edu-servers.net. 172800 IN A 192.33.14.30
c.edu-servers.net. 172800 IN A 192.26.92.30
...
Here’s the DNS response from the root name server.
DNS Lookup Walkthrough
Here’s the DNS header.
Here’s the 16-bit ID number in the DNS header.
Here are the flags in the DNS header.
Here are the record counts in the DNS header.
Here’s the DNS payload. It’s a collection of resource records (one per line), sorted into four sections.

## Slide 33
$ dig +norecurse eecs.berkeley.edu @198.41.0.4
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 26114
;; flags: qr; QUERY: 1, ANSWER: 0, AUTHORITY: 13, ADDITIONAL: 27
;; QUESTION SECTION:
;eecs.berkeley.edu. IN A
;; AUTHORITY SECTION:
edu. 172800 IN NS a.edu-servers.net.
edu. 172800 IN NS b.edu-servers.net.
edu. 172800 IN NS c.edu-servers.net.
...
;; ADDITIONAL SECTION:
a.edu-servers.net. 172800 IN A 192.5.6.30
b.edu-servers.net. 172800 IN A 192.33.14.30
c.edu-servers.net. 172800 IN A 192.26.92.30
...
DNS Lookup Walkthrough
Here’s the question section. The name is eecs.berkeley.edu, the type is A, and the value is blank. It shows that we are looking for the IP address of eecs.berkeley.edu.
The answer section is blank, because the root name server did not return the answer we’re looking for.
We can confirm this by checking the header, which says there are 0 records in the answer section.
The authority and additional sections tell the resolver where to look next.
Note that there are multiple .edu name servers for redundancy.
For redundancy, there are usually several name servers for each zone. Any of them will usually work. Let’s pick the first one.
This NS record says that a.edu-servers.net is a .edu name server.
This A record helpfully tells us the IP address of the next name server we mean to contact.

## Slide 34
$ dig +norecurse eecs.berkeley.edu @198.41.0.4
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 26114
;; flags: qr; QUERY: 1, ANSWER: 0, AUTHORITY: 13, ADDITIONAL: 27
;; QUESTION SECTION:
;eecs.berkeley.edu. IN A
;; ANSWER SECTION:
eecs.berkeley.edu. 86400 IN A 23.185.0.1
...
DNS Lookup Walkthrough
The answer section has one A type record. It tells us that the IP address of eecs.berkeley.edu is 23.185.0.1.
Here’s the time-to-live (TTL) field in the record. It tells us that we can cache this answer for 86,400 seconds (24 hours).
In the case of a positive response with address